## Slide 1: Off Grid communications with Android
m0nk and stoker have fun @ DefCon 20
- Meshing the mobile world

## Slide 2: Who are you guys?
m0nk – Josh Thomas
  jthomas@accuvant.com
  m0nk.omg.pwnies@gmail.com
Stoker – Jeff Robble
  jrobble@mitre.org
  mistr.stoker@gmail.com
We work(ed) @ The MITRE Corporation (of CVE fame)
Notes: m0nk & Stoker

## Slide 3: tl; dr:
  https://github.com/monk-dot
Notes: m0nk

## Slide 4: A placeholder so m0nk can babble
Notes: m0nk asks why we need another Mesh talk?
If you do mesh and I don’t mention you, please don’t get pissed. Instead, email me and we can chat.
If all you want to do is WiFi tether, please don’t… it’s cool I guess, but really boring.

## Slide 5: Where data goes to die
Fukushima
Katrina
Haiti
< Insert your “favorite” recent natural disaster here >
Other?
Notes: m0nk

## Slide 6: Why do I care about Mesh networks?
Physical infrastructure is prone to failure, networks shouldn’t be
Bypass the Cellular networks
Bypass Wi-Fi networks
Share information when infrastructure is broken or untrustworthy
Extend and bounce other networks via bridging / tethering
Headless
Notes: m0nk

## Slide 7: Ok, kind of cool. What about “Off Grid”?
Single point of failure = single point of sniffing / filtering
I don’t trust someone else being able to turn off my network, do you?
When you want to share info, but don't want anyone watching 
Notes: m0nk

## Slide 8: There should really be a funny pic below
Notes: m0nk talks about Kansas City

## Slide 9: Your pocket contains more than a consumption device for Grumpy Fowl
Wi-Fi chip with a fairly fat pipe
Cell modem and baseband processor
A ton of sensors
(Somewhat) quality NAND and RAM
A very under clocked and underutilized processor
Power
A boring screen that blinks!
Notes: m0nk

## Slide 10: The SPAN framework
We did the boring stuff so you don’t have to!
General Overview of the framework, what / why / how
  Harnessing SPAN for your own project?
  Repurpose root to muck with your Wi-Fi chipset
Notes: Next 10 minutes overview slide

## Slide 11: SPAN + Android Technical Architecture
Blinkie on a Map
Java Networking Interface
TCP Socket
UDP Socket
MANET Service
Reliable Transmission Layer
Security Manager
Session Manager
P2P Chat App.
Other App.
Network Configuration
Modular MANET Routing Protocol Framework
Manual Routing Protocol Selection
Automated Routing Protocol Selection
Proactive Routing Protocol Manager
Reactive Routing Protocol Manager
OLSR
BATMAN
Protocol 3
DSR
Protocol 2
Protocol 3
iptables / netfilter
Linux Kernel Routing
Transparent Proxy
Notes: Stoker
OLSR – Optimized Link State Routing
BATMAN - Better Approach To Mobile Ad-hoc Networking
DSR – Dynamic Source Routing
tproxy is based on monoutil and requires netfilter queue rules setup by iptables to direct packets to it

## Slide 12: Data Flow
P2P Chat App.
Java Networking Interface
Transparent Proxy
Reliable Transmission Layer
MANET Routing Protocol
P2P Chat App.
Java Networking Interface
“Hello!”
Source Node
Relay Node
Destination Node
[determine route]
[update network topology]
Transparent Proxy
Reliable Transmission Layer
MANET Routing Protocol
Transparent Proxy
Reliable Transmission Layer
MANET Routing Protocol
[update network topology / determine route]
Transparent Backend
Notes: Stoker

## Slide 13: Why we love Broadcom
Flipping chipsets into Ad-Hoc Mode
Notes: Stoker

## Slide 14: Kernel v. Metal
Dear Vendors: Please either stop mucking with your kernel source or provide it to the community
Notes: Stoker

## Slide 15: Ad-hoc Mode
Leveraged Wi-Fi Tether for Root Users app.
  Edify script for setting up ad-hoc mode using cross-compiled iwconfig
Some phone wi-fi drivers don’t support ad-hoc mode
  Wi-Fi Tether app. switched to using softAP
  softAP: software enabled portable wireless access point
Needed to compile Wireless Extensions support into kernel
  Compiled vendor open source software
  Dumped zImage and drivers to AnyKernel tree
  Flashed using ClockworkMod Recovery
https://github.com/koush/AnyKernel
Notes: Stoker
  Used arm cross compiler and Linux menuconfig
Wi-Fi modes: Ad-Hoc, Managed, Master, Repeater, Secondary (repeater), Monitor, or Auto

## Slide 16: Why we love Broadcom
Flipping chipsets into Ad-Hoc Mode
Notes: Stoker

## Slide 17: Kernel v. Metal
Dear Vendors: Please either stop mucking with your kernel source or provide it to the community.
Notes: Stoker

## Slide 18: Where are my packets?
Android <= 4.0 (ICS) devices filter out UDP broadcasts when the screen is off
  WifiManager.WifiLock doesn’t help
First approach: Force screen to always stay dimmed even when user presses power button
  Create wakelock
    powerManager.newWakeLock(PowerManager.SCREEN_DIM_WAKE_LOCK | PowerManager.ACQUIRE_CAUSES_WAKEUP, “ADHOC_WAKE_LOCK”)
  Register an IntentFilter for Intent.ACTION_SCREEN_OFF
  Acquire wakelock when intent received
Notes: Stoker
  Could receive TCP just fine

## Slide 19: Where are my packets?
Second approach: Set dhd_pkt_filter_enabled=0 when loading wi-fi kernel module
  Required recompiling Galaxy Nexus wi-fi driver
Notes: Stoker

## Slide 20: Plug and Play / Dynamic routing algorithms and you!
Adjusting packet routing at runtime, a 5 minute primer on untrustworthy routing tables
The tradeoffs of Bandwidth vs. Network Scale and Multi-Hop headaches
File share, Chat, Disconnected Twitter and VOIP over a Mesh. Oh, the fun we can have.
Notes: Next 10 minutes overview slide

## Slide 21: This slide should not be needed
What do I use a network for?
  Chat
  Data and file sharing
  VoIP
  Situational Awareness and Crisis management
  Disconnected Twitter
Notes: m0nk?

## Slide 22: Ad-Hoc Network Routing 101
Why BATMAN is better than OLSR?
Notes: m0nk?

## Slide 23: Definitions
A
B
D
C
A
B
D
C
A
B
D
C
Topology
Route to
1-hop neighbor
Route to 2-hop
neighbor
Notes: Stoker
Directed vs. non-directed
A route consists of edges

## Slide 24
Optimized Link State Routing Protocol (2003)
Link-state protocol
  Nodes know who they can talk to
  Each node calcs entire route to every other node
Proactive
  Routes periodically planned in advance
  Kernel-level routing table modified on-the-fly
Dijkstra Open Shortest Path First algorithm
Layer 3 in OSI stack
http://www.ietf.org/rfc/rfc3626.txt
Notes: Stoker
No special network API required since kernel-level routing table is modified
Nodes only share edge info, not routes

## Slide 25
A
Hello.A
Hello.A
Hello.A
Hello.A
Hello.A
Hello.A
Hello.A
Hello.A
B
B
A
Find 1-hop neighbors
B
A
Hello.B
B
A
Asymmetric Link
Asymmetric Link
B
A
Symmetric Link
Notes: Stoker
Hello TTL=2

## Slide 26
A
Hello.A
Hello.A
Hello.A
Hello.A
Hello.A
Hello.A
Hello.A
Hello.A
B
B
C
A
Hello.A
Find 2-hop neighbors
C
B
C
A
Notes: Stoker
Hello TTL=2
Assumes B and C are symmetric neighbors

## Slide 27
B
C
A
D
E
Multi-Point Relay
A selects B as MPR
  All 2-hop nodes reachable through B
All > 1-hop routes from A will go through B
F
Notes: Stoker
Hello TTL=2
Assumes B and C are symmetric neighbors
Global topology info is > 2 hops away
MPRs are not always chosen if network is small

## Slide 28: OLSR
Pros
  Better than everyone sharing everything
    Topology info dumps only between MPRs
  Incremental improvements
Cons
  MPRs are throughput choke points
    Isolated points of failure
  Entire routes planned in advance, but next hop doesn’t care about your route, it uses its own
Notes: Stoker
MPRs intended to be reliable/powered/stationary nodes; not realistic in a smart-phone ad-hoc network

## Slide 29: BATMAN
Better Approach to Mobile Ad-hoc Networking (2006)
Next-gen OLSR
Decentralize: No single point has all the data
  No MPRs
  Each node sends out originator msgs: “I exist”
  Every other node keeps track of number of hops an originator msg took to reach them
http://www.open-mesh.org/projects/open-mesh/wiki/The-olsr-story
Notes: Stoker
Also, there’s a layer 2 (ethernet) implementation: batman-adv

## Slide 30: BATMAN
  Simplify: Only plan first step in route
  Direct packets along route with lowest originator msg. hop count
Notes: Stoker

## Slide 31: Where Are We Today?
  OLSR still the most popular
  BATMAN gaining traction
  We can do better and so can you
    If you are working in the space, please email us.
Notes: Stoker

## Slide 32: Smart Phones Have Sensors!
Battery
  Don’t send packets to phones going dead
  Send more packets to phones plugged in
GPS
  Form routes to phones closer to you
  Form routes to phones that don’t move often
Accelerometer
  Don’t send packets to phones in motion
  Predict phone movement and send packets to phones moving in the right direction
Notes: m0nk

## Slide 33: Reactive Protocols
Stale routing table = What routing table?
No we can play with motion and location in a useful way
Don’t forget that if you pack node location into the headers it can been seen by others
Downsides come with throughput issues
Notes: m0nk & Stoker

## Slide 34: An aside on Delay tolerance
Disconnected nodes act as disjoint message queues
The protocol thinks of the device as a carrier pigeon (RFC 2549)
Fall back to message passing
Notes: m0nk

## Slide 35: Scale, Delay and Hopping
Though we see great improvements, simple proactive routing uses a ton of bandwidth to stabilize the network
  Still, we can predict bandwidth and throughput metrics
  VoiP good until we scale quite large
Reactive routing has less chatter with the same bandwidth but is laggy
Mix them FTW.
Notes: m0nk & Stoker

## Slide 36: More Tunnels and some preliminary Security
Jumping over the cell network or Wi-Fi (Mimicking VPN with standard Tunnels)
Tunneling the mesh through the Internets!
  VPN clusters and remote enclaves
Securing the mesh from unwanted guests
Jumping through unsecured mobile nodes
Notes: Next 10 minutes overview slide

## Slide 37: Jumping over the cell network or Wi-Fi
Your phone has at least 2 network ports (Wi-Fi & Cell):
  We can connect them
  We can bridge them
Tablet with no cell chip?
  Plug in an ALFA wireless USB dongle
Virtual mesh networks connected using simple VPN tunnels
Notes: m0nk & Stoker

## Slide 38: IP Address Assignment
  Static IP assignment
  Generate a unique IP based on phone MAC address, IMEI, etc.
  DHCP requires a server or global knowledge of IPs in use
Notes: Stoker

## Slide 39: A Security Paradigm?
Use Bluetooth or NFC to Bump transfer configuration info and keys
Secure each link / node with its own keys
Encrypt network data such that bounce or hop nodes cannot decrypt
Notes: m0nk & Stoker

## Slide 40: Security
Share symmetric key in config file distributed in-person via NFC
Symmetric encryption using P2P Diffie-Helman key exchanges
Asymmetric encryption using public / private key pair
A third party certificate authority isn’t practical
Notes: Stoker

## Slide 41: Security
http://servalpaul.blogspot.com/2012/04/making-security-simple.html
Serval public keys double as network addresses
256-bit Curve25519 public keys based on the CryptoBox NaCl crypto library
Network intrinsically distributes keys!
Uses CryptoBox authenticated encryption for unicast traffic
Uses CryptoSign verified signing for publicly readable broadcast traffic
CryptoSign uses a handwritten sign to confirm identity
Notes: Stoker

## Slide 42: ICS & Wi-Fi Direct: android.net.wifi.p2p API
“Provides classes to create peer-to-peer (P2P) connections over Wi-Fi Direct”
Initial ICS drop is a very lame partial implementation of the spec
  Kind of works like Bluetooth pairing
  Wi-Fi doesn’t support connecting to an AP and P2P at the same time
Possible upgrade in JB?
Notes: Stoker
Turn on Wi-Fi direct and immediately disconnected from AP
“internet of Things”
Wi-Fi direct spec states that Wi-Fi chips will be able to send packets using multiple MAC addresses at once

## Slide 43: Root required
Need root to modify iptables / routing tables
Need root to mess with Wi-Fi driver and put phone in ad-hoc mode
Grab Zerg, wrap in APK and pop the phone on install
Over the Air install?
Notes: m0nk + Stoker

## Slide 44: What about my…?
A:
  iPhone: In Theory
  Black Berry: Maybe?
  Windows Phone: Yes (why do you own one?)
  Arduino / GumStix: Yes
  Netbook / Linux / Mac / Windows Box: Yes
  Toaster: Yes but Why?
Framework is a mix of Java and C
  If your box can run those…
Notes: m0nk

## Slide 45: iOS?
Apple gave us a built in Wi-Fi proxy configurable with the iPhone Configuration Utility
Ooohhh, is that an APN setting as well?
Cool, now all we need is a simple server to proxy and route our data
Notes: m0nk

## Slide 46
Notes: m0nk

## Slide 47: What else can we use the Mesh for?
Mobile data redundancy using the Torrent protocol to raid data across all devices?
Distribute threads and tasks across a cloud of unused processors?
Spoofing?
Notes: m0nk

## Slide 48: Similar Projects
Collaboration?
Notes: Stoker
Also based on Wireless Tether for Root Users app.

## Slide 49: Freifunk
http://wiki.freifunk.net/
http://berlin.freifunk.net/
German for "Free radio”
Non-commercial open grassroots initiative to support free open radio networks in Germany
Offers specialized OpenWrt-firmware
  Routing based on OLSR or BATMAN
Freifunk Berlin has 500+ nodes
Notes: Stoker
Users register for a Freifunk Berlin IP using an online webform

## Slide 50
http://www.servalproject.org/
Android ad-hoc network framework
Implemented features
  VOIP calls between Serval Mesh-enabled phones
  MeshMS, free mesh-based SMS
Features under development
  Serval Rhizome, distributed mesh-based data distribution platform
  Serval Maps, mesh-based mapping application
  Serval Morse, distributed micro-blogging service
  A simple API for using Serval services
Notes: Stoker
Also based on Wireless Tether for Root Users app.
Dr. Paul Gardner-Stephen
Also called batphone

## Slide 51: Future Work
VOIP over the mesh
IP address assignment
Evaluate and improve Serval’s approach to security
iOS and Windows 8 port
Notes: Stoker
Servers are bad in a P2P network
IMEI: International Mobile Equipment Identity

## Slide 52: Dumb enough to attempt a demo!
Oh wait, we already did?
Notes: Stoker

## Slide 53: Shameless Plug
GitHub repo:
  https://github.com/monk-dot
Notes: Stoker

## Slide 54: Open Source Projects Used
Wireless Tether for Root Users
  “This program enables tethering (via wifi) for rooted handsets.”
  http://code.google.com/p/android-wifi-tether/
olsrd
  “An adhoc wireless mesh routing daemon”
  http://www.olsr.org/
monoutil
  “A simple tool for network monitoring” using netfilter
  http://code.google.com/p/monoutil/
Processing for Android
  “Processing is a language and environment for people who want to create images, animations, and interactions.”
  http://wiki.processing.org/w/Android
Linux: iwconfig, iptables, dnsmasq, tcpdump, etc.
Notes: Stoker